EEG Measurement Protocol for Tactile Stimulation with Strong Electromagnetic Noise
(2025/12/11 - BEPG)
1. Objective
Establish a robust and reproducible method to isolate the neural response to tactile stimulation (e.g. ~22 Hz and other selected frequencies) while suppressing strong electromagnetic (EM) noise generated by tactors and background noise.
Note that you not chose 25Hz, 50 Hz, 75 Hz, 100 Hz …
Core strategy:
 baseline → epoching → normalization → contrasting
2. Baseline Material and References
The following sources form the theoretical and methodological baseline:
Video introduction / conceptual background:
https://www.youtube.com/watch?v=7ahrcB5HL0k
Time–frequency and neural signal analysis reference:
 https://direct.mit.edu/books/monograph/4013/Analyzing-Neural-Time-Series-DataTheory-and
BCI and EEG resources:
 https://github.com/NeuroTech-Leuven/bci-resources?tab=readme-ov-file

3. Experimental Conditions
Two well-controlled conditions are required to achieve a baseline. These map directly onto the previously described test positions.
3.1 Condition 1: Finger-On-Tactor (FOT)
Finger rests directly on the mechanical contact nipple of the tactor.
- True tactile stimulation is present.
- Electromagnetic noise from the tactor is present.
- EM noise from the environment is present
3.2 Condition 2: IFNFN (Finger In Noise Field, Not Feeling Nipple)
Finger placed in the same EM field generated by the tactor, without receiving tactile stimulation.
Implemented as one of the following equivalent configurations:
- Finger next to the contact nipple but still within the EM field.
- Finger on a mechanically identical tactor with the contact nipple removed or disabled.
This condition preserves EM noise while eliminating tactile input and is the critical control condition.
Only one factor may differ between conditions: presence vs absence of tactile stimulation.
Option: White noise headset (auditive stimulation)
Option: Visual stimulation (of the tractor without)

4. Hardware Options
4.1 Tactors (3 configurations)
- Medical-grade tactor (low EM noise; limited availability) with Differential Coil Design.
- Consumer-grade tactor
- Consumer-grade tactor with and without contact nipple
4.2 Additional Components
- Shielded cables (mandatory)
- Optional filters (to be evaluated)
Hardware filtering:
- Hardware filters may be used for denoising signals after the Class D amplifier of VBS.
- Any hardware filter must be explicitly validated to ensure it does not distort amplitude, phase, timing, or relevant spectral content of the stim frequency.
4.3 Two-Channel Considerations
- Preferred setup uses two tactors:
  - FOT tactor (functional nipple)
  - IFNFN tactor (identical EM behavior, disabled/removed nipple)
- Assumes similar EM field emission; this must be verified empirically.

5. Positioning and Mechanical Control

The finger position must be identical across conditions.
- Standard tractor: with or without tractor
  - Remove the nipple, double sided tape
- Use a fixed finger cradle, alignment marker, or 3D‑printed finger bed.
Distance and orientation relative to the tactor must not vary.
Mechanical consistency is essential to ensure that the contrast isolates neural effects rather than positioning artifact
6. Test Procedure
6.1 Number of Cycles / Trials
- Absolute minimum: 50 cycles
  - SNR changes with * 7
- Target / best practice: 100 cycles per condition
  - SNR changes with * 10
6.2 Switching Schemes (in order of preference)
1. Randomized sequence
  1. Subject is prompted via screen to place the finger in the correct position.
  2. Minimizes expectancy and behavioural bias.
2. Alternating sequence (1 → 2 → 1 → 2)
  1. Screen prompts required to maintain timing and pacing.
3. Blocked batches
  1. 20 cycles of condition 1, followed by 20 cycles of condition 2, repeated.
4. Fully blocked
  1. 100 cycles of condition 1, followed by 100 cycles of condition 2.
  2. Least preferred, but currently the only option supported by the existing sweep software.

7. Timing and Triggering
7.1 Triggering
- A software trigger marks the exact start of stimulation (t = 0).
- Extreme sub-millisecond precision is not required (not an ERP paradigm).
- Known event timestamp bugs must remain fixed.
7.2 Recommended Timing
- Pre-stimulation baseline: ≥ 1 s
- Stimulation duration: ~4 s per trial
- Post-stimulation recording:
  - Optional, but recommended when studying resonant frequencies or post-stimulus effects.

8. Epoching Strategy
Epochs are created separately for conditions 1 and 2.
- Baseline window: −1.0 s to −0.5 s relative to STIM‑ON
- Stimulation window: +0.5 s to +X.0 s
Notes:
- Data immediately around t = 0 must be excluded due to filter and wavelet smearing.
- Trimming applies symmetrically before and after STIM‑ON to ensure clean state separation.

9. Data Processing Pipeline (Time–Frequency Domain)
Step 1 — Full Time–Frequency Transform
Apply TFR (e.g. Morlet wavelets, MNE TFR) to the entire recording.
Output: channels × time × frequency.
Step 2 — Epoching
Epoch around triggers using the windows defined above.
Step 3 — Baseline Normalization
Use ratio, log-ratio, or dB normalization.
Purpose:
- Removes general EEG noise
- Suppresses slow drifts
- Reduces EM and environmental noise common to both conditions
Step 4 — Contrasting
Compute:
- Mean TFR(FOT)
- Mean TFR(IFNFN)
Then compute:
Contrast = FOT − IFNFN
This cancels:
- EM noise from the tactor
- Environmental noise
- Non-task-related brain activity
- Variance caused by finger proximity
Result:
Isolated neural response attributable to tactile stimulation.

10. Sweep Software Requirements
- Current sweep software only supports the fully blocked protocol (100 cycles 1 → 100 cycles 2).
- Supporting any other switching scheme requires:
  - Major revision or full redesign
  - Extension of marker handling and trial logic

11. Test Protocol Script
- The original test protocol script is stored in OneDrive.
- This script must be upgraded to:
  - Support additional switching schemes
  - Expose richer marker information
  - Align explicitly with this integrated protocol

12. Test Facility Considerations
- At KULLAB, no second wall penetration is available.
- EEG cables are forced to run close to noisy tactor cables, which is suboptimal.
- A test run using the team’s own system should be considered for comparison.
- Any future use of KULLAB requires paid rental.
- We consider also BRAINSHUB
  https://gbiomed.kuleuven.be/english/research/50000737/research/50487173/brainshub/BHaddress

13. Frequency Selection
- Frequencies must be selected conservatively due to the high number of cycles required.
- Avoid frequencies that are divisors of 50 Hz to minimize power-line contamination.
- Prioritize frequencies of strongest theoretical and physiological relevance.

14. Recommended Workflow Summary
Preparation
- Build 2‑channel setup (FOT + IFNFN tactors).
- Ensure fixed finger positioning.
- Define randomized or semi-randomized trial schedule.
Recording
- Software trigger at t = 0.
- Record baseline + stimulation + optional post-stimulus.
- Collect 50–100 trials per condition.
Analysis
- Compute TFR on full recording.
- Epoch around triggers.
- Apply baseline normalization.
- Average per condition.
- Compute FOT − IFNFN contrast.
The resulting signal represents the clean neural response to tactile stimulation under strong EM noise conditions.